# What's RFID?
Radio-frequency identification (RFID) is the use of a wireless non-contact system that uses radio-frequency electromagnetic fields to transfer data from a tag attached to an object, for the purposes of automatic identification and tracking.

# What is NFC
Near field communication (NFC) is a set of communication protocols that enable two electronic devices, one of which is usually a portable device such as a smartphone, to establish communication by bringing them within 4 cm (2 in) of each other.

# RFID Hardware
## Reader/Writer
### Touch-a-tag

C3L is in possession of several Touchatag readers which work fine on Linux (after some hacking)
getdigital.de
### ACR122U

A good piece of hardware with a good linux support.
### Proxmark

Works like a charm under linux!
## NFC Tags

### NTAG216
Those are the NFC tags we use to chip our Hackerspace passports.
Capacity: 888 Byte.
Standard: NFC Forum Type 2 Tag ISO 14 443 A
nfc-mfultralight r dump.mfd
nfc-mfultralight w dump.mfd
# RFID Software
## libnfc
sudo apt-get install libnfc-dev
## RFIDIOt
A bunch of python scripts. Preinstalled on Kali linux.
## mfoc
Mifare Classic Offline Cracker is a tool that can recover keys from Mifare Classic cards.
Website
## mfcuk
Installation procedure was from 2012. Now the installation is straight forward!

MFCUK - MiFare Classic Universal toolKit. Toolkit containing samples and various tools based on and around libnfc and crapto1, with emphasis on Mifare Classic NXP/Philips RFID cards.
Special emphasis of the toolkit is on the following:
- mifare classic weakness demonstration/exploitation
- demonstrate use of libnfc (and ACR122 readers)
- demonstrate use of Crapto1 implementation to confirm internal workings and to verify theoretical/practical weaknesses/attacks
Website
### mfoc & mfcuk installation guides
#### Ubuntu
Install the pcscd package.
sudo apt-get install pcscd
Install libccid
sudo apt-get install libccid
Install autoreconf
sudo apt-get install autoreconf
Install libnfc-1.3.9
autoreconf -vis
./configure
make
sudo make install
Download mfoc
autoreconf -vis
./configure
make
sudo make install
If you encounter problems after the execution, do this:
sudo ln -s /usr/local/lib/libncf.so* /usr/lib/
Now mfoc should be up and running.
Download and install libnfc-1.5.1
autoreconf -vis
./configure
make
sudo make install
Download mfcuk
svn checkout http://mfcuk.googlecode.com/svn/trunk/ mfcuk-read-only
Symlink shared object libs!
sudo ln -s /usr/local/lib/libncf.so* /usr/lib/
Install mfcuk
autoreconf -vis
automake --add-missing
autoconf
./configure
Now open the Makefiles in /mfcuk-read-only & /mfcuk-read-only/src and search for the line LIBS = .Replace it with:
LIBS = $(LIBNFC_LIBS)
Now…
make
sudo make install
Final step
cd /mfcuk-read-only/src
cp data /usr/local/bin
Now you should be ready for ownage!